## Slide 1
AI-Powered RTL Verification & Debugging Platform
SystemVerilog • Icarus Verilog • GTKWave • FastAPI • GraphQL • Neo4j • Groq • Streamlit
Traffic Light Controller + 4-bit ALU

## Slide 2
1. Problem & Objective
Traditional RTL Verification
Run simulations repeatedly
Read logs to identify failures
Inspect waveforms manually
Trace failures back to the design
My Platform
Automates simulation
Parses PASS/FAIL
Stores verification relationships
Adds AI-assisted debugging
Outcome
Clear verification results
Traceability in Neo4j
Root-cause explanation
Debugging recommendation
Important: PASS/FAIL comes from the simulator + testbench. AI is used only after a failure.
2

## Slide 3
2. Complete System Architecture
Streamlit
GraphQL
FastAPI
Verification Service
Icarus Verilog
Simulation
Neo4j AuraDB
PASS
FAIL
Store verification result
Groq AI → Root Cause → Recommendation → Neo4j
3

## Slide 4
3. RTL Example — Two-Road Traffic Light Controller
SystemVerilog RTL
FSM + Counter
A_GREEN
A_YELLOW
B_GREEN
B_YELLOW
Clock
Counter counts cycles
FSM decides WHAT state Counter decides WHEN to change
Traffic-light outputs
Four states: A_GREEN → A_YELLOW → B_GREEN → B_YELLOW
Counter controls how long each state remains active
Testbench checks state sequence and timing
4

## Slide 5
4. RTL Example — 4-bit ALU
A[3:0]
B[3:0]
Opcode[1:0]
4-bit ALU
result[3:0]
00 → ADD
01 → SUB
10 → AND
11 → OR
Example: A=6, B=3, OR → expected 7
5

## Slide 6: Bit Sizes & Worked Examples
1. ALU — 4 bits
A = 0101 (5)
B = 0011 (3)
ADD: 0101 + 0011 = 1000 (8)
AND: 0101 & 0011 = 0001 (1)
OR: 0101 | 0011 = 0111 (7)
2. FSM State — 2 bits
4 states need 2 bits.
00 → A_GREEN
01 → A_YELLOW
10 → B_GREEN
11 → B_YELLOW
Sequence: 00 → 01 → 10 → 11 → 00
3. Counter — 3 bits
3 bits represent 0–7.
For a 5-cycle state:
000 → 001 → 010 → 011 → 100 → 101
At count 4, transition can occur.
4. ALU Opcode — 2 bits
4 operations need 2 bits.
00 → ADD
01 → SUB
10 → AND
11 → OR
Example: opcode 11 selects OR.
Failure examples: Traffic Light → expected A_YELLOW, actual B_GREEN (COUNTER_ERROR). ALU OR → expected 7, actual 2 (OUTPUT_MISMATCH).

## Slide 7
5. Testbench & Verification
1. Apply inputs
2. Run RTL
3. Calculate expected
4. Compare
5. PASS / FAIL
The SystemVerilog testbench acts as the verifier.
It gives inputs, waits for output, and compares expected vs actual.
PASS/FAIL is deterministic and does not come from the LLM.
The testbench can also generate a VCD waveform for debugging.
Verification = checking whether the hardware behaves according to its specification.
6

## Slide 8
6. Simulation, Log Parser & GTKWave
RTL + Testbench
Icarus Verilog
Simulation
simulation.log → Log Parser → structured PASS/FAIL
waveform.vcd → GTKWave → signal behavior over time
Log Parser reads simulator text such as TEST_1: PASS / TEST_3: FAIL.
It converts text into total, passed, failed, expected and actual values.
VCD stores signal changes; GTKWave visualizes clock, state, counter, inputs and outputs.
Example failure: Expected = 7, Actual = 2 → OUTPUT_MISMATCH
7

## Slide 9
7. Backend, GraphQL & Neo4j
Streamlit
GraphQL
FastAPI
Neo4j AuraDB
FastAPI manages the backend and starts verification jobs.
GraphQL is the query layer between Streamlit and FastAPI; the frontend requests the fields it needs.
Neo4j stores connected verification information as nodes and relationships.
Project
RTL
Verification Job
Simulation
Failure
Project → Job → Simulation → Tests / Failures → AI Analysis
8

## Slide 10
8. Failure Analysis with Groq AI
Simulator/Testbench finds failure
Log Parser + Failure Analyzer
Groq AI
Root Cause + Recommendation
Traffic Light Failure
Expected: A_YELLOW
Actual: B_GREEN
Category: COUNTER_ERROR
AI: counter threshold is incorrect
ALU Failure
A=6, B=3, operation=OR
Expected: 7 Actual: 2
Category: OUTPUT_MISMATCH
AI: OR was implemented using AND
AI explains WHY a test failed; it does not decide PASS/FAIL.
9

## Slide 11
9. Demo Flow, Results & Key Takeaway
1
Select design
2
Run verification
3
Icarus simulates
4
Read PASS/FAIL
5
Inspect GTKWave
6
View Neo4j + AI
Traffic Light — PASS
4 tests • 4 PASS • 0 FAIL
Traffic Light — FAIL
4 tests • 2 PASS • 2 FAIL
ALU — FAIL
OR • Expected 7 • Actual 2
SystemVerilog verifies hardware → Icarus simulates → Log Parser structures results → Neo4j preserves traceability → Groq explains failures → GraphQL/Streamlit present the result.
10